## Slide 1: Router Design
By: Kumar Sai Reddy Guntaka
Instructor: Orod Haghighiara
Date: 12/05/2022

## Slide 2: Introduction:
Routing is the act of transporting a data packet from its origin to its destination, allowing messages to move from one computer to another and finally reach the destination system. A router is a networking device that transmits data packets from one computer network to another. It is linked to two or more data lines from several networks (as opposed to a network switch, which connects data lines from one single network).

## Slide 3: Cisco Packet Tracer

## Slide 4: FSM:

## Slide 5: State1: Decode address
FSM is the monitoring and controlling unit of the router architecture.
State1: Decode_Address -> initial reset state
Signal detect_add is asserted in this state which is used to detect an incoming packet. It is also used to latch the first byte as a header byte.

## Slide 6
State 3: Load_data and first data
The first data byte to the FIFO. Signal busy is also asserted in this state so that header byte that is already latched doesn’t update to a new value for the current packet.
This state is changed to LAOD_DATA state unconditionally in the next clock cycle.
State2: Wait_till_empty
Signal busy is de asserted in this state, so that ROUTER can receive the new data from input source every clock cycle,
Signal write_enb_reg is asserted in this state in order to write the Packet information (Header+Payload+Parity) to the selected FIFO.
This state transits to LAOD_PARITY state when pkt_valid goes low and to FIFO_FULL_STATE when FIFO is full.

## Slide 7
State4&8: Load parity, check parity error
In this state the last byte is latched which is the parity byte. It goes unconditionally to the state CHECK_PARITY_ERROR.
Signal busy is asserted so that ROUTER doesn‟t accepts any new data. write_enb_reg is made high for latching the parity byte to FIFO.
State5: FIFO full state
Busy signal is made high and write_enb_reg signal is made low.
Signal full_state is asserted which detects the FIFO full state.

## Slide 8
Load after full state:
The data after FIFO_FULL_STATE. Signal busy & write_enb_reg is asserted. It checks for parity_done signal and if it is high, shows that LOAD_PARITY state has been detected and it goes to the state DECODE_ADDRESS.
If low_packet_valid is high it goes to LOAD_PARITY state otherwise it goes back to the LOAD_DATA state.

## Slide 9: FSM

## Slide 10: REGISTER

## Slide 11: SYNCHRONIZER
Detect_add and data_in signals are used to select a FIFO till a packet routing is over for the selected FIFO.
Signal fifo_full signal is asserted based on full_status of fifo_0 or FIFO_1 or FIFO_2.
If data_in =2‟b00 then fifo_full=full_0
If data_in=2‟b01 then fifo_full=full_1
If data_in=2‟b10 then fifo_full=full_2 else fifo_full=0
The signal vld_out_x signal is generated based on empty status of the FIFO as shown below :
vld_out_0=~empty_0
vld_out_1=~empty_1
vld_out_2=~empty_2
The write_enb_reg signal is used to generate write_enb signal for the write operation of the selected FIFO.

## Slide 12: FIFO Block:
The FIFO works on the system clock and is reset
with a synchronizer active low reset.The FIFO is also internally reset by an internal reset signal soft_reset. Soft_reset is an active high signal which is generated by the SYNCHRONIZER block during time out state of the ROUTER. If resetn is low then full=0, empty=1 and data_out=0.
Write_Operation: Signal data_in is sampled at the rising edge of the edge of the clock when write_enb is high. Write operation only takes place when FIFO is not full in order to avoid over_run condition.
Read_Operation: Data out is driven to HIGH impedance state under 2 scenarios: When the fifo m/m is read completely (header+payload+parity).
Under the time out condition of the Router. Full- FIFO status which indicates that all the locations inside FIFO have been written. Empty- FIFO status which indicates that all the locations of the FIFO have been read and made empty. Read and write operation can be done simultaneously.

## Slide 13: Top Module Output Protocol:

## Slide 14: Top Module

## Slide 15: References
[1] Priyanka Rakshe and Pankaj Prajapati," "Router1x3 Protocol design with Virtual cut through Mechanism for Network on Chip (NoC)", Journal of Emerging Technologies and Innovative Research
[2] Ramya. C.B, Chethan. C.M, Praveen. S.G, Rakshith S, "Design and Implementation of Spartan 6 Series FPGA Board and Application of PID Controller for Robots", International Journal of Recent Advances in Engineering & Technology (IJRAET) Volume-3, Issue -5, 2015\
[3] Router 1X3 – RTL Design
[4] https://www.khanacademy.org/computing/computers-and-internet
[5] Neso Academy: https://www.youtube.com/watch?v=xwaqSZHK8eM

## Slide 16: Thank you